## Slide 1: Bangladesh Climate-Resilient Ecosystem Curriculum (BACUM)
Module 3: Forest Carbon Measurement and Monitoring

## Slide 2: Module 3: Forest Carbon Measurement and Monitoring
SECTION II: FOREST CARBON STOCKS AND IPCC GUIDELINES
2.2. Land Use, Land Use Change, and Forestry (LULUCF)

## Slide 3: Forest Carbon Measurement and Monitoring (FCMM)
FUNDAMENTALS OF FOREST CARBON IN REDD+ CONTEXT
  1.1. Forests, the Global Carbon Cycle and Climate Change
  1.2. The Roles of Forests and Forest Carbon in Global Climate Negotiations
  1.3. Challenges for Forest-based Climate Change Mitigation
FOREST CARBON STOCKS AND IPCC GUIDELINES
  2.1. Overview of Forest Carbon Pools (Stocks)
  2.2. Land Use, Land Use Change, and Forestry (LULUCF)
  2.3. IPCC Guidelines for Forest Carbon Measurement and Monitoring
  2.4. Reference Levels – Monitoring against a Baseline
FOREST CARBON MEASUREMENT AND MONITORING METHODS
  3.1. Overview of Forest Carbon Measurement and Monitoring
  3.2. Quality Assurance and Quality Control (QA/QC)
  3.3. Field Sampling Design Methods
  3.4. Forest Carbon Field Measurement Methods
  3.5. Carbon Stock Calculation and Available Tools
  3.6. Creating Activity Data and Emissions Factors
  3.7. Considerations in Developing a Monitoring System

## Slide 4: Acknowledgements
UNIVERSITIES
Bangladesh Agricultural University
University of Chittagong
Dhaka University
Independent University, Bangladesh
Khulna University
Noakhali University of Science and Technology
Shahjalal University of Science and Technology
Sher-e-Bangla Agriculture University
North South University
EXPERT CONTRIBUTORS | SPECIFIC INPUTS
Prof. (Dr.) Manzoor Rashid | Curriculum Development for all topics
Prof. (Dr.) Md. Danesh Miah | REDD+, Forest Carbon
Prof. (Dr.) Md. Jakariya | Community NR Management, Climate Change, Natural Resources Management
DESIGN, LAYOUT AND CONTENT DEVELOPMENT: Ms. Chi Pham, Curriculum Development Expert, Bangkok, Thailand
CREL STAFF | CREL STAFF
John A Dorr | Utpal Dutta
Abu Mostafa Kamal Uddin | Ruhul Mohaiman Chowdhury
Kevin T. Kamp | Rahima Khatun
Paul Thompson | Sultana Razia Zummi
Abdul Wahab | Shams Uddin
Shahzia Mohsin Khan | 

## Slide 5: Learning Objectives
By the end of the session, students will be able to:
Link Land Use, Land Use Change and Forestry (LULUCF) to carbon emission/sequestration
Characterize role of anthropogenic perturbations to the global carbon cycle
Compare regional and country specific patterns in forest cover and land use cover change
Identify key drivers of deforestation and forest degradation in Bangladesh

## Slide 6: Anthropogenic Perturbation of the Global Carbon Cycle Averaged globally for the Decade 2002 – 2011 (PgC/yr)
Source: Le Quéré et al. (2012); Global Carbon Project (2012)
Notes: KEY MESSAGES:
The arrows to the atmosphere from fossil fuel burning and cement production as well as land use change represent the major human perturbations to the global carbon cycle.
The numbers beside each arrow indicate the amount of carbon transferred annually in gigatonnes. The diagram shows that there are pathways out of the atmosphere (or sinks) for a large fraction of the carbon emitted from human activities. It is important as well to note the size of the fluxes associated with human activities as compared to the “natural” fluxes from the vegetation and ocean ( on the order of 100 gigatonnes per year each). The fluxes from human activities are 10 fold smaller but have a large impact because they are not balanced by an equal flux out of the atmosphere!
Note in the lectures for CMM deck on the carbon cycle was covered in detail and if you have not used those lectures in your course you may want to borrow one or more slides to make sure the students understand the carbon cycle
Reference:
Carbon Dioxide Information Analysis Center http://cdiac.ornl.gov/GCP/#
Global Carbon Project http://www.globalcarbonproject.org/
Image source :
Le Quéré et al. (2012); Global Carbon Project (2012)

## Slide 7: Global Carbon Cycle – Anthropogenic Perturbation (2002 - 2011)
+
28%
46%
26%
Atmospheric growth
Fossil fuels and cement
Land-use change
Land sink
Ocean sink
90%
(1.0 ± 0.5 PgC/yr)
10%
(2.5 ± 0.5 PgC/yr)
Sources: Le Quéré et al. 2012; Global Carbon Project 2012
(2.6 ± 0.8 PgC/yr)
(4.3 ±0 .1 PgC/yr)
(8.3 ± 0.4 PgC/yr)
Notes: KEY MESSAGES:
Approximately half of the carbon emitted from human activities remains in the atmosphere: one-quarter is taken up by the ocean and one-quarter is thought to be taken up by vegetation.
CO2 emissions from fossil fuels burning and cement production in 2011 increased 54% over 1990, with a total of 9.5±0.5 PgC emitted to the atmosphere (34.7 billion tones of CO2).
CO2 emissions from deforestation and other land-use change were 1.0±0.5 PgC in 2011. For the period 2002-2011, land-use change emissions accounted for 10% of all emissions from human activity (fossil fuel, cement, land-use change).
Reference and Images source:
http://www.globalcarbonproject.org/carbonbudget/index.htm

## Slide 8: Change in Forest Area Caused by LUC
  Increasing forest area
  Decreasing forest area
Notes: KEY MESSAGES:
Land Use Change (LUC) includes both changes that increase forest cover and decreases it and can be driven by natural or human factors
Notes:
Shown here is a simplified model illustrating forest change dynamics. It has only two classes: forests and all other land. A reduction in forest area can happen through either of two processes: deforestation and natural disasters. Deforestation, which is by far the most important, implies that forests are cleared by people and the land converted to another use, such as agriculture or infrastructure. Natural disasters may also destroy forests, and when the area is incapable of regenerating naturally and no efforts are made to replant, it too converts to other land covers (examples such as desertification).

## Slide 9: Land Use Change, CO2 Emissions
Notes: KEY MESSAGES:
In the earlier slide we saw that emissions from land use change, primarily cutting and burning of forests, represent about 10% of total emissions due to human activities but land use change associated emissions are concentrated in tropical regions as shown in this map and for some countries may be the major source of greenhouse gas emissions from human activities.
Emissions of carbon dioxide due to changes in land use mainly come from the cutting down of forests and using the land for agriculture or built-up areas, urbanization, roads etc. When large areas of rain forests are cut down, the land often turns into less productive grasslands with considerably less capacity of storing CO2.
Image source:
http://www.grida.no/graphicslib/detail/co2-emissions-from-land-use-change_f0e2

## Slide 10: Land-Use Change, CO2 Emissions
Peat fires
Source: Global Carbon Project (2012)
A general decrease in emissions since 1990
Black line: Includes management-climate interactions; Thin line: Previous estimate
Notes: KEY MESSAGES:
The data suggest an overall decrease trend in land-use change emissions particularly since 2000.
Notes:
CO2 emissions from deforestation and other land-use change were 0.9±0.5 PgC in 2011.
For the period 2002-2011, land-use change emissions accounted for 10% of all emissions from human activity (fossil fuel, cement, land-use change).
The implementation of new land policies, higher law enforcement to stop illegal deforestation, and new afforestation and regrowth of previously deforested areas could all have contributed to this decline.
Total emissions from human activity in 2011 (fossil fuel, cement, land-use change) were 10.4±0.7 PgC.
Emissions from land-use change were 36% of the total human emissions in 1960, 18% in 1990, and 9% in 2011.
Uncertainty for all land-use change emission estimates remains large.
CO2 emissions from land-use change are mainly based on forest statistics of the FAO and a bookkeeping method, and include interannual variability in deforestations based on fire activity from year 1997 onwards.
Graph source:
Global Carbon Project (2012)
http://www.globalcarbonproject.org/carbonbudget/index.htm
Bottom Photo Source:
http://www.sylvanheightshomestay.com/location.asp

## Slide 11: Review: Land Use VS Land Cover
Land Cover
Land use VS Land cover?
Notes: KEY MESSAGES:
It is important to understand the difference between land use and land cover. An example map of each is given here. Ask students to discuss what they think is covered by each term
Notes:
After the discussion you can give them the following definitions
Land use:
Areas are classified based on the purpose the land serves: such as recreation, wildlife habitat or agriculture
Classifications do not necessarily describe the surface cover on the ground
Land cover:
Areas are classified based on the surface cover on the ground whether vegetation, urban infrastructure, water, bare soil or others
Classification do not describe the use of land. Areas with the same land use classification may be used very differently.
Definitions source:
http://msue.anr.msu.edu/news/the_difference_between_land_use_and_land_cover
Image source:
Land cover map SE Asia: http://bioval.jrc.ec.europa.eu/products/veget_map_continental-sea/continentalSEasia.php
Land use map of Korea:http://www.cotf.edu/ete/modules/korea/landuse.htm

## Slide 12: Class Exercise: Group Discussion
Using the FAO Charts have students answer the following two questions
Which region has the largest forest cover in the world?
Which region has the least forest cover in the world?
Notes: KEY MESSAGES:
Have students determine which regions have the largest and smallest amount of forest cover and have them either discuss or vote on their findings depending on the size of the class
Chart source:
FAO. 2010. Forest Genetic Resources Assessment 2010: Main Report. Food and Agriculture Organization of The United Nations, Rome.

## Slide 13: Distribution of Forests by Region /Sub-region in 2010
Source: FAO (2010)
Notes: KEY MESSAGES:
Currently forests cover 31% of the Earth’s land mass with Europe (including Russia) holding the largest fraction followed by South America and Oceania as a region having the smallest fraction
Notes:
All 233 countries and areas reporting for FRA 2010 provided information on the extent of forests.
The total forest area in 2010 was estimated to be 4 billion hectares.
Chart source:
FAO. 2010. Forest Genetic Resources Assessment 2010: Main Report. Food and Agriculture Organization of The United Nations, Rome

## Slide 14: Distribution of Forest Area by Region in 2010
Chart: 
| Africa | Asia | Europe | N & C America | S America | Oceania
Forest area | 17 | 15 | 25 | 17 | 21 | 5
Source: Data from FAO (2010)
Notes: KEY MESSAGES:
This pie chart shows the same information: Europe (including Russia) holds 25% of the world’s forest area followed by South America (21%). Oceania holds 3% of the global forest area.
Reference:
Graph generated for this presentation by RECCD participants using data from FAO. 2010. Forest Genetic Resources Assessment 2010: Main Report. Food and Agriculture Organization of The United Nations, Rome

## Slide 15: Distribution of Forest Area by Country in 2010
Ten countries with the largest forest area
Russia
Brazil
Others
Source: Data from FAO (2010)
Notes: KEY MESSAGES:
Moving from Region to country we see the Russia holds the most forest cover followed by Brazil, Canada and the US
Notes:
Countries with large amounts of forest area have the potential for large emissions associated with land-use change if those forests are cut and/or burned and converted to other uses.
The amount of forest area is only one factor- another important factor are the drivers
Graph source:
FAO. 2010. Forest Genetic Resources Assessment 2010: Main Report. Food and Agriculture Organization of The United Nations, Rome

## Slide 16: Deforestation
Notes: KEY MESSAGES:
Forest area has been reduced in every region of the world. The pink/beige area shows original forest extent and the dark green the current forest extent
Notes: Forest area has been reduced everywhere forests naturally occur
Map source:
http://uclast203-2010.wikispaces.com/Deforestation+of+the+Amazon produced by Allianz
Alternative map source:
http://www.lgm-interactive.com/wp-content/uploads/2011/09/Allianz_deforestation1.jpg

## Slide 17: Class Exercise: Group Discussion
Objective:
  To identify the difference in deforestation rate in different regions
Activity
  Rank the regions listed on the following slide from highest to lowest rate of deforestation for the period 2000-2010
  Let a representative of each group present and share their result (10 minutes)
Notes: KEY MESSAGES:
Let students separate into groups and rank the regions on the following slide based on the FAO charts
Let representative of each group present and share their results. (all should take about 10 mins)

## Slide 18: Rates of Global Deforestation
Africa
Asia
Oceania
South America
North and Central America
Europe
Number & rank the highest rates to lowest rates for each region 2000 - 2010
Notes: KEY MESSAGES:
Here are the regions to be considered in the class activity

## Slide 19: Annual Change in Forest Area by Region and Sub-region in 1990-2010
Source: FAO (2010)
Notes: KEY MESSAGES:
This table provides some answers to students. Note that some areas are increasing in forest area!!!
Notes:
The total net change in forest area in the period 2000–2010 is estimated at -5.2 million hectares per year.
South America suffered the largest net loss of forests between 2000 and 2010 – about 4.0 million hectares per year – followed by Africa, which lost 3.4 million hectares annually. Compare net loss in ha to percent loss who are the leaders there?
Table source:
FAO. 2010. Forest Genetic Resources Assessment 2010: Main Report. Food and Agriculture Organization of The United Nations, Rome

## Slide 20: Annual Change in Forest Area by Region in 1990-2010
Source: FAO (2010)
Notes: KEY MESSAGES:
Here is the same information as in the last slide, but in graph form.
Notes:
We see Europe and Asia have net increase in forest area, North America has neither gained nor lost in the past decade. Africa and South America have seen significant losses of forest area. Note losses of forest area indicated deforestation- they give no indication of the quality of forest cover in the areas still deemed
Chart source:
FAO. 2010. Forest Genetic Resources Assessment 2010: Main Report. Food and Agriculture Organization of The United Nations, Rome

## Slide 21: Deforestation and Forest Degradation
Notes: KEY MESSAGES:
In the case of forest degradation the area remains in forest but forest structure and composition is changed which affects its capacity to function and from the human perspective its ability to provide ecosystem services. Various definitions of degraded forest can be found at http://www.fao.org/docrep/009/j9345e/j9345e08.htm
In the images in this slide it is easy to distinguish deforested areas from forest but the differences between degraded and intact forest are more subtle. See if students have some ideas about why forest degradation occurs- what are the activities that result in degraded forests?
Image source:
http://news.mongabay.com/2011/0208-camara_inpe_interview.html

## Slide 22: Class Exercise: Group Discussion
Objective:
  To identify and prioritize drivers of deforestation and forest degradation in SEA
Activity:
  Prioritize 3 key drivers of deforestation in SEA
  Prioritize 3 key drivers of forest degradation in SEA, Present the group’s result
Time:
  30 minutes
Notes: KEY MESSAGES:
Make sure students are comfortable with drivers as a concept. This can be done as individuals or in small groups depending on the size of the class.

## Slide 23: Drivers of Deforestation & Forest Degradation
DEFORESTATION
Agriculture (commercial)
Agriculture (local/subsistence)
Infrastructure
Mining
Urban expansion
FOREST DEGRADATION
Timber logging
Fuel wood charcoal
Uncontrolled fires
Livestock grazing in forests
Notes: KEY MESSAGES:
Here a list of the most important drivers of deforestation and forest degradation globally.
Compare the group’s result with the global rivers of deforestation/forest degradation. Remember you asked students to focus on South East Asia and these drivers are global

## Slide 24: Drivers of Deforestation – Area Proportion
Notes: KEY MESSAGES:
This graph shows the effect of the major drivers of deforestation by area in each of the three major tropical regions.
Notes:
This graph shows how much deforestation is attributed to each of the major drivers in the three major tropical regions. In all three regions Agriculture is a prime driver of deforestation though the role of commercial (export) and subsistence (local) agriculture differs. The other drivers are currently only causing minor rates of deforestation
Chart source:
Kissinger, G., M. Herold, V. De Sy. 2012. Drivers of Deforestation and Forest Degradation: A Synthesis Report for REDD+ Policymakers. Lexeme Consulting, Vancouver.

## Slide 25: Drivers of Deforestation - Proportion
Notes: KEY MESSAGES:
The patterns are a bit clearer when we look at drivers as proportion of total rather than on net area
Commercial agriculture is much more important in Latin America driven by soy production primarily in Brazil while in Africa and Asia local agriculture is responsible for a larger fraction of deforestation Note the importance of urban expansion in Asia
Chart source:
Kissinger, G., M. Herold, V. De Sy. 2012. Drivers of Deforestation and Forest Degradation: A Synthesis Report for REDD+ Policymakers. Lexeme Consulting, Vancouver.

## Slide 26: Drivers of Forest Degradation - Proportion
Notes: KEY MESSAGES:
For deforestation we found that agriculture was a key driver in all three tropical regions. For degradation logging is a universal driver though in Africa it is second to fuelwood/ charcoal
Reference:
http://iopscience.iop.org/1748-9326/7/4/044009/article
Chart source:
Kissinger, G., M. Herold, V. De Sy. 2012. Drivers of Deforestation and Forest Degradation: A Synthesis Report for REDD+ Policymakers. Lexeme Consulting, Vancouver.

## Slide 27: Take Home Message
Human activity has a small but significant impact on the global carbon cycle
Deforestation and land use change currently account for approximately 10% of the human perturbation of the global carbon cycle
Agriculture is the major driver of deforestation in all three tropical regions while logging is the major driver of forest degradation.
Identifying key drivers of deforestation & forest degradation could better protect/manage forests, thus reducing CO2 Emissions and increasing Carbon sequestration.
Notes: KEY MESSAGES:
Three major points from this lecture- make sure students also understand how shift in land use with its associated shift in terrestrial carbon pools is related to emissions.

## Slide 28: References and Resources
USAID. 2015. USAID LEAF‘s Climate Change Curriculum. USAID Lowering Emissions in Asia Forests Program (USAID LEAF). Winrock International and US Forest Service. Bangkok, Thailand.
FAO. 2010. Forest Genetic Resources Assessment 2010: Main Report. Food and Agriculture Organization of The United Nations, Rome.
FAO. 2012. Community Guidelines for Accessing Forestry Voluntary Carbon Markets. RAP Publication 2012/16. Food and Agriculture Organization of The United Nations, Rome.
Trumper, K., Bertzky, M., Dickson, B., van der Heijden, G.,Jenkins, M., Manning, P. June 2009. The Natural Fix? The Role of Ecosystems in Climate Mitigation. A UNEP Rapid Response Assessment. United Nations Environment Programme, UNEPWCMC, Cambridge.
Le Quéré, C., R. Andres, T. Boden, T. Conway, R. Houghton, J. House, G. Marland, G. Peters, G. van der Werf, A. Ahlström, R. Andrew, L. Bopp, J. Canadell, P. Ciais, S. Doney, C. Enright, P. Friedlingstein, C. Huntingford, A. Jain, C. Jourdain, E. Kato, R. Keeling, K. Klein Goldewijk, S. Levis, P. Levy, M. Lomas, B. Poulter, M. Raupach, J. Schwinger, S. Sitch, B. Stocker, N. Viovy, S. Zaehle and N. Zeng (2012), “The Global Carbon Budget 1959–2011”, Earth System Science Data Discussions (in review), http://www.earth-syst-sci-data-discuss.net/5/1107/2012, DOI:10.5194/essdd-5-1107-2012
Global Carbon Budget. 2012. Carbon Budget 2012: An Annual Updates of Global Carbon Budget and Trends. Available Source: http://www.globalcarbonproject.org/carbonbudget/index.htm.
Kissinger, G., M. Herold, V. De Sy. Drivers of Deforestation and Forest Degradation: A Synthesis Report for REDD+ Policymakers. Lexeme Consulting, Vancouver.
GRID-Arendal website: http://www.grida.no/publications/rr/natural-fix/page/3724.aspx
Earthlabs website: http://www.grida.no/publications/rr/natural-fix/page/3724.aspx

## Slide 29: References and Resources
The curriculum of USAID’s Climate-Resilient Ecosystems and Livelihoods (CREL) in Bangladesh is a free resource of teaching materials for university professors, teachers and climate change training experts.
Reproduction of CREL’s curriculum materials for educational or other non-commercial purposes is authorized without prior written permission from the copyright holder, provided the source is fully acknowledged.
Suggested citation: Winrock International. 2016. USAID‘s Climate-Resilient Ecosystems and Livelihoods (CREL). Winrock International. Dhaka, Bangladesh.
Disclaimer: The CREL’s curriculum is made possible by the support of the American People through the United States Agency for International Development (USAID). The contents of the curriculum do not necessarily reflect the views of USAID or the US Government.

## Slide 30: USAID's Climate-Resilient Ecosystems and Livelihoods (CREL) Project Winrock International Headquarters 2101 Riverfront Drive, Little Rock Arkansas 72202-1748 USA Tel: 1-501-280-3000 Web: www.winrock.org