## Slide 1: Bangladesh Climate-Resilient Ecosystem Curriculum (BACUM)
Module 3: Forest Carbon Measurement and Monitoring

## Slide 2: Module 3: Forest Carbon Measurement and Monitoring
SECTION III: FOREST CARBON MEASUREMENT AND MONITORING METHODS
3.1. Overview of Forest Carbon Measurement and Monitoring

## Slide 3: Forest Carbon Measurement and Monitoring (FCMM)
FUNDAMENTALS OF FOREST CARBON IN REDD+ CONTEXT
  1.1. Forests, the Global Carbon Cycle and Climate Change
  1.2. The Roles of Forests and Forest Carbon in Global Climate Negotiations
  1.3. Challenges for Forest-based Climate Change Mitigation
FOREST CARBON STOCKS AND IPCC GUIDELINES
  2.1. Overview of Forest Carbon Pools (Stocks)
  2.2. Land Use, Land Use Change, and Forestry (LULUCF)
  2.3. IPCC Guidelines for Forest Carbon Measurement and Monitoring
  2.4. Reference Levels – Monitoring against a Baseline
FOREST CARBON MEASUREMENT AND MONITORING METHODS
  3.1. Overview of Forest Carbon Measurement and Monitoring
  3.2. Quality Assurance and Quality Control (QA/QC)
  3.3. Field Sampling Design Methods
  3.4. Forest Carbon Field Measurement Methods
  3.5. Carbon Stock Calculation and Available Tools
  3.6. Creating Activity Data and Emissions Factors
  3.7. Considerations in Developing a Monitoring System

## Slide 4: Acknowledgements
UNIVERSITIES
Bangladesh Agricultural University
University of Chittagong
Dhaka University
Independent University, Bangladesh
Khulna University
Noakhali University of Science and Technology
Shahjalal University of Science and Technology
Sher-e-Bangla Agriculture University
North South University
EXPERT CONTRIBUTORS | SPECIFIC INPUTS
Prof. (Dr.) Manzoor Rashid | Curriculum Development for all topics
Prof. (Dr.) Md. Danesh Miah | REDD+, Forest Carbon
Prof. (Dr.) Md. Jakariya | Community NR Management, Climate Change, Natural Resources Management
DESIGN, LAYOUT AND CONTENT DEVELOPMENT: Ms. Chi Pham, Curriculum Development Expert, Bangkok, Thailand
CREL STAFF | CREL STAFF
John A Dorr | Utpal Dutta
Abu Mostafa Kamal Uddin | Ruhul Mohaiman Chowdhury
Kevin T. Kamp | Rahima Khatun
Paul Thompson | Sultana Razia Zummi
Abdul Wahab | Shams Uddin
Shahzia Mohsin Khan | 

## Slide 5: Learning Objectives
At the end of this session, students will be able to:
Describe fundamental concepts and technical options for the measurement and monitoring of forest carbon,
Explain the components of carbon stock inventories
Apply the principles of remote sensing for forest carbon monitoring

## Slide 6: Why are Carbon Measurement and Monitoring Important?
Notes: KEY MESSAGES:
Measurement and monitoring of terrestrial carbon pools particularly forest carbon pools are important for three major reasons: size of these pools, rate of flux from these pools and role of terrestrial carbon management in climate change mitigation
The image here shows that the combined vegetation and soil pools are much larger than the surface ocean or atmospheric pools and the fluxes from the terrestrial carbon pools to and from the atmosphere are as large as those to the surface oceans. While fluxes from land use change are smaller than from fossil fuel burning they still represent approximately 10% of the unbalanced flux and management of fluxes to and from the terrestrial pools especially the vegetation pools must be part of any climate change mitigation plan
Image source:
https://www.carboncyclescience.us/what-is-carbon-cycle

## Slide 7: Importance of Terrestrial Carbon Measurement and Monitoring
The key challenges for implementing LULUCF mitigation:
  To develop credible baselines of carbon emissions
  To monitor the changes in carbon stocks over the length of the project
  In order to meet these challenges we need to:
  Identify which carbon stocks need to be measured in the project
  To measure carbon stocks accurately to a known level of precision
Notes: KEY MESSAGES:
To include management of forest carbon pools as a major component of climate change mitigation credible estimates of current pools and fluxes in and out of these pools are essential.
IPCC has specific good practice guidelines for measurement and monitoring of emissions from LULUCF.
Acronyms:
LULUCF = land use land use change and forestry.
References:
See this link for LULUCF definitions: www.ipcc-nggip.iges.or.jp/public/gpglulucf/gpglulucf_files/Chp1/Chp1_Overview.pdf
See this link for the LULUCF good practice guidance Summary for Policy Makers from 2000: https://www.ipcc.ch/pdf/special-reports/spm/srl-en.pdf

## Slide 8: Carbon Accounting for Land Use Change
Estimates of carbon emissions depend on two factors:
1. The amount of area undergoing a specific transition- this is called the Activity Data
2. The change in carbon pools association with that transition- this is called the Emissions Factor
Notes: KEY MESSAGES:
In carbon accounting two terms are fundamental to the discussion: Activity Data and Emissions Factors.
Estimates of carbon emissions depend on two factors: 1. The amount of area undergoing a specific transition- this is called the Activity Data 2. The change in carbon pools association with that transition- this is called the Emissions Factor
Here are simple definitions to introduce the concepts.
Deforestation map source:
WWF Greater Mekong Programme, Ecosystems in the Greater Mekong Report -- http://awsassets.panda.org/downloads/greater_mekong_ecosystems_report_020513.pdf
Deforestation image source: http://www.umt.edu/ethics/debating%20science%20program/odc/climatechange/climatealternatives/reduceddeforestation.php

## Slide 9: Carbon Emission Calculation
Activity data | * | Emission factor | = | Emissions from Deforestation
1000 ha | * | 495 t CO2/ha | = | 495,000 t CO2e
Notes: KEY MESSAGES:
This is how we use both Activity data and Emission factors to calculate emissions from land use change
Notes:
We are going to examine how biomass measurements and carbon calculations are used to build emissions factors for different land use transitions and also how to determine activity data. This slide illustrate the example of emissions; activity data and emission factor. Important to again highlight that the units are tons of CO2 equivalent.
The concept of CO2 equivalency is explained at this link: http://en.wikipedia.org/wiki/Carbon_dioxide_equivalent:
Carbon dioxide equivalency (CO2e) is a quantity that describes, for a given mixture and amount of greenhouse gas, the amount of CO2 that would have the same global warming potential (GWP), when measured over a specified timescale (generally, 100 years). Carbon dioxide equivalency thus reflects the time-integrated radiative forcing of a quantity of emissions or rate of greenhouse gas emission—a flow into the atmosphere—rather than the instantaneous value of the radiative forcing of the stock (concentration) of greenhouse gases in the atmosphere described by CO2e.
Activity Data (AD): The area of land undergoing the transition in question
Emission Factor (AF): The amount of carbon released when an area is converted from one land use to another
Reference:
USAID LEAF's Training. 2013

## Slide 10: Methods and Framework for Terrestrial Carbon Measurement and Monitoring
Methods for terrestrial carbon measurement
  Field measurements or inventories
  Remote sensing
  Models
Approaches for monitoring periodic changes in carbon pools
  Gain-loss
  Stock change
Notes: KEY MESSAGES:
There are a number of different methods and frameworks commonly used for the measurement and monitoring of carbon pools.
Notes:
In the next set of slides we will present the various methods briefly. The approaches to monitoring shifts in carbon pools is covered in the lectures of deck 4 and are not covered in this lecture.

## Slide 11: Field Measurements or Inventories
Measurements done in-situ and converted into biomass and carbon estimates using conversion (allometric) equations
Measurements of carbon density, areal extent and change over time (if measured more than once)
Notes: KEY MESSAGES:
Field measurements are the most direct. Biomass can be measured directly or indirectly through measures of proxies such as tree diameter and in some cases heights. Samples from other pools (soils, herbaceous biomass etc) may also be collected for measurement. Biomass is then converted into carbon pools based on carbon density.
Notes: In Deck 4 there are much more detailed explanations of field measurement approaches.
Image source:
http://www.metla.fi/bulletin/2010/capacity.html

## Slide 12: Field Sampling Framework
Sampling system
  simple random sampling
  Systematic sampling
  stratified random sampling
  cluster sampling
Plot shape and size
Number and distribution of sampling units
Notes: KEY MESSAGES:
The first step in setting up a field sampling framework is determination of the sampling approach including plot size shape and number as well as how they will be distributed across the study area. These decisions are based on information about the study area as well as considerations of cost and access.
Detailed information on field sampling frameworks and developments are given in slide decks 4.2 and 4.3
Inventory plot map from:
http://www.fs.fed.us/ne/fia/spatial/examples.html
Sample plot graphic from:
Walker et al. 2012, Standard Operating Procedures for Terrestrial Carbon Measurement Winrock International

## Slide 13: Which Pools to Measure?
Above-ground biomass
Below-ground biomass
Dead wood
Litter
Soil organic carbon
Harvested forest products
Notes: KEY MESSAGES:
In addition to deciding on the plot size, number of plots, etc discussed in the previous slide, before starting a field measurement campaign a decision needs to be made as to which carbon pools will be measured. The decision is usually based on which pools are largest and which pools are most subject to change (especially if setting up a repeated measurement monitoring framework)
Notes:
In forests woody aboveground biomass mass is almost universally measured as it is often the largest pool and one of the most easily measured. This image is from an earlier lecture where we discussed the major carbon pools in forests ( lecture 2.1). Review with students which pools are usually the largest and which ones are most likely to change
Image source:
Vickers, B. et al. 2012. Community guidelines for accessing forestry voluntary carbon markets Chapter 1 Forests and Climate Change FAO Regional Office for Asia and the Pacific. http://www.fao.org/docrep/016/i3033e/i3033e01.pdf

## Slide 14: Measurement Methods for Above-ground Biomass
Destructive method
  Harvest method
Non-destructive method
  Allometric method
Notes: KEY MESSAGES:
Aboveground biomass as the largest and often most rapidly changing pools is measured in all forest inventories. There are two classes of methods: destructive methods and non-destructive methods commonly based on relationships between diameter and height and biomass.
Notes:
This photo and the one on the next slide show the destructive method
Image source:
Peter Umunay http://environment.yale.edu/tri/fellow/1908/

## Slide 15: Destructive Harvest Methods
Harvest the tree (and/or other living above-ground material) and determine biomass by weighing all components (stem, branches, and foliage).
Notes: KEY MESSAGES:
Destructive methods as suggested by their name require that the biomass be cut down or harvested and then weighed to determine mass.
Advantage: The most accurate method within a small unit area
Disadvantages: Expensive, time consuming, damaging to the environment and infeasible at large scale or for projects where accumulation of carbon or biomass is the goal
Commonly used: to calibrate allometric methods- by building accurate relationships between easily measured non destructive indices such as diameter and biomass (allometric equations) the information obtained by destructive methods can be used at large scales to relatively easily and cheaply estimate biomass without harvesting the biomass
Image source:
http://blog.worldagroforestry.org/index.php/2014/03/10/kill-the-tree-to-save-it/

## Slide 16: Non-destructive or Allometric Methods
Conduct a field inventory, where data are collected at plot level on species or site-specific factors (species, stem density, DBH, height etc.)
Apply appropriate equations or models to convert these measurements into biomass estimates
Notes: KEY MESSAGES:
Non-destructive approaches use relationships developed from destructive sampling to allow measurements of indices ( usually diameter at breast height with height sometimes included) to calculate biomass.
Notes:
Typically, the more site-specific variables that are measured at site, the more accurate the biomass estimate will be. Relationships developed for individual species and specific site conditions (climate soils etc) are more accurate than general equations.
Image source:
Walker et al. 2012. Standard Operating Procedures for Terrestrial Carbon Measurement. Winrock. Accessible at http://www.leafasia.org/tools/winrock-standard-operating-procedures-terrestrial-carbon-measurementfield-sop-manual or at http://www.winrock.org/sites/default/files/publications/attachments/Winrock_Terrestrial_Carbon_Field_SOP_Manual_2012_Version.pdf

## Slide 17: Allometric Equations Used to Estimate Stock
Equations used to estimate biomass stocks from field measurements (DBH and H), or to estimate below ground (root) biomass
where:
  Y = biomass (kg/tree)
  X = D (diameter, cm), D2, or D2H where H is height in m
  a, b = constants
Notes: KEY MESSAGES:
This is the general form of the equations used to relate diameter or height (or both) to biomass for individual trees.
Notes:
An allometric equation for the relationship between tree diameter and total tree mass is developed by destructively harvesting a sample of trees across a representative range of diameter classes. Then the diameter of the trees can be measured, and the formula applied to estimate total mass of the trees in the area.

## Slide 18: Examples of an Allometric Relationship for Above- Ground Biomass
Above-ground biomass
Notes: KEY MESSAGES:
Here is an example of the data from 454 trees destructively sampled used to develop allometric equations-
Notes:
Discuss the implications of the r2 value and look at where the variation mostly occurs ( high diameter individuals)
This example is from hardwood stands in the eastern US and developed by Winrock International
Image source:
Schroeder et al. 1997 Forest Science 43: 424-434

## Slide 19: Examples of Default Equations for Above-ground Biomass
Source: Brown (1997)
Notes: KEY MESSAGES:
The table gives examples of default allometric equations
Notes:
In the cases where site-specific equations do not exist, it is possible to use an average equation- site and species specific equations are missing for many species and sites
Table source:
Brown, S. 1997. Estimating biomass and biomass change of tropical forests: a primer. FAO Forestry Paper 134, Rome, Italy.

## Slide 20: Common Types of Conversion Equations Applied for Forest Carbon Measurement
Notes: KEY MESSAGES:
The table summarizes some common types of conversion equations that can be applied Individually, or in combination to calculate biomass and carbon pools.
Chart source:
Havemann, T. 2009. Measuring and Monitoring Terrestrial Carbon: The State of the Science and Implications for Policy Makers ion to calculate biomass and carbon pools. Report for the Terrestrial Carbon Group and the UNREDD Programme

## Slide 21: Class Exercise 1. Pre-class Assigned Reading
Objective: To characterize role of remote sensing in terrestrial carbon measurement
Pre-class assigned reading: Measuring and Monitoring Terrestrial Carbon: The State of the Science and Implications for Policy Makers (Topic 2.2 Remote sensing)
Notes: Pre-readings required
Time: 30 mins
If you have the opportunity have the students read the text before the lecture an alternate activity is suggested on the next slide if this is not feasible.

## Slide 22: Class Exercise Pre-class assigned reading
Separate students into three groups and present to answer the following questions
  Q: What is remote sensing?
  Q: How does remote sensing work?
  Q: How remote sensing can be applied for terrestrial carbon measurement?
Learners to present the questions and share their answer in class
Time: 30 minutes
Notes: Alternate suggestion: If you cannot have the students do the pre-reading an alternative is to watch the video on the following slide that gives a brief summary of remote sensing and how it works.
Time: 30 mins

## Slide 23: What is Remote Sensing (RS)
The technology of acquiring information about the earth's surface (land and ocean) and atmosphere , using sensors onboard airborne (aircraft, balloons) or space borne (satellites, space shuttles) platforms.
http://www.crisp.nus.edu.sg/~research/tutorial/intro.htm
Notes: KEY MESSAGES:
Remote sensing is a broad category which includes data from a variety of airborne and space borne sensors
After the students discuss their answers to the class exercise discuss this definition and see if students can name some common remote sensing applications Lectures in section 4 will go into more detail about remote sensing and the actual sensors here we are primarily giving students a sense of applications
Images source:
http://www.crisp.nus.edu.sg/~research/tutorial/opt_int.htm

## Slide 24: How does Remote Sensing Work?
The raw “data” from remote sensing are in the form of microwave, optical or infrared radiation reflected or scattered back by the imaged area in the direction of the sensor.
Sensors differ in terms of measured wavelengths; energy source, resolution (spectral, spatial, radiometric and temporal resolution), costs and data interpretation requirements.
Notes: KEY MESSAGES:
Remote sensing data are usually represented as images and often confused with photographs. Sensors detect various wavelengths of radiation either simply emitted or reflected back from the surface of the object being detected.
Notes: Remote sensing does require specialized technical skills and can be expensive in terms of both data acquisition and interpretation.

## Slide 25: Remote Sensing: What Can RS Do?
Measure areal extent, volume and change over time (if measured more than once)
Notes: KEY MESSAGES:
Remote sensing is frequently used to monitor land cover at large spatial scales. Repeated measures on a daily monthly or annual timestep allows for estimation of the areal extent of land cover change. You may have heard of or read about Landsat or MODIS images which are commonly used to estimate land cover.
The image here shows the change in albedo classes near Ho Chi Minh city Vietnam
Reference:
Citation
Nguyen-Thanh Son ; Chi-Farn Chen ; Cheng-Ru Chen ; Li-Yu Chang and Bui-Xuan Thanh "Urban growth mapping from Landsat data using linear mixture model in Ho Chi Minh City, Vietnam", J. Appl. Remote Sens. 6(1), 063543 (Jun 21, 2012). ;

## Slide 26: Applications of RS in Estimating Land Use/Land Cover Change
Well-suited to capturing large scale events (e.g. Deforestation)
Also can be applied to capturing smaller scale events (e.g. degradation and intensification or agricultural changes) but that requires more detailed data and data interpretation, including more intensive non-destructive field measurements.
www.geology.com
Notes: KEY MESSAGES:
Remote sensing has traditionally been used to complement intensive field surveys working at larger spatial scales than can be feasibly done with field surveys (regional to national and larger scales).
Initially work was done on events that caused clear signals such as forest clearing and conversion to pasture. Recently improved signal detection and data interpretation has allowed work to be done at smaller spatial scales and on more subtle changes in forest structure ( ie forest degradation)

## Slide 27: Applications of RS in Estimating Land Use/Land Cover Change
www.geology.com
http://earthobservatory.nasa.gov/Features/Deforestation/deforestation_update4.php
This map shows percent forest cover in eastern Democratic Republic of the Congo. Red areas, expanding outward from the town of Mambasa, show deforestation between 1990 and 2000.
Notes: KEY MESSAGES:
Here is an example from Congo. Overlaying images of forest cover from 1990 and 2000 allows the mapping of forest cover change
The areas in red in the image above are the areas where forests were cut.
Reference:
Image retrieved from http://earthobservatory.nasa.gov/Features/Deforestation/deforestation_update4.php

## Slide 28: Applications of RS in Estimating Carbon Density and Changes in Density
Directly - based on quantifiable relationships between biomass and spectral responses
Indirectly - based on classification techniques, indices and regression equations or models developed through research pairing field measurements with remote sensing reflectance measurements.
www.geology.com
Notes: KEY MESSAGES:
Data from remote sensing can be used to calculate variables other than vegetation cover. Using direct and indirect techniques information about carbon stocks can be inferred.
In addition to changes in forest cover RS can be used to determine carbon density and changes in carbon density. There are several ways that remote sensing imagery can be used to estimate carbon density and changes in carbon density. Methods for estimation of C density and changes can be divided into two major groups direct and indirect approaches

## Slide 29: Applications of RS in Estimating Carbon Density and Changes in Density
www.geology.com
Forest carbon mapping in Borneo 1982- 2008
Notes: KEY MESSAGES:
Here is an example of a carbon density change map from Borneo- The research team used NDVI (normalized difference vegetation index) data from a number of different sensors to determine forest cover and then estimated carbon pool changes based on the relationship between forest cover and carbon pools
Historical deforestation (forest degradation and regeneration) on Borneo Island was estimated using the time-series remote-sensing data (MODIS, SPOT, PALSAR). Figure 4 shows the time series of forest cover change during the last three decades (1982 – 2008). In each area where a forest cover decrease was detected, the ecosystem model estimated immediate carbon emissions due to the forest decrease (deforestation or forest degradation), followed by gradual carbon absorption due to the forest re-growth.
Image source:
http://www.earthzine.org/2010/09/21/forest-carbon-mapping-using-remote-sensed-disturbance-history-in-borneo/

## Slide 30: Applications of RS in Estimating Non-biomass Pools
Australia’s soil carbon baseline mapped
www.geology.com
Notes: KEY MESSAGES:
Additionally remote sensing can be used to estimate non-biomass forest carbon pools both indirectly using known relationships with measured above-ground biomass and directly as in the case for soil carbon
Notes:
This is an example of soil carbon mapping from remote sensing. This work required three major datasets on soil carbon from field surveys as well as remote sensing information on reflectance.
Estimation of SOM using remote sensing has relied on the strong relationship between the quantity of SOM and soil colour (visible reflectance). The more direct visible reflectance method of estimating SOM requires visibility of bare ground. As with remote sensing of ABG biomass, good calibration and ground truthing are essential. There are limitations for estimating SOM based on soil reflectance which is a function of many factors in addition to organic matter, including soil moisture, texture, chemical composition, parent material and surface conditions. Complications are magnified when it is necessary to map a large geographical area
Image from:
http://www.csiro.au/Organisation-Structure/Flagships/Sustainable-Agriculture-Flagship/Australian-Soil-Carbon-Map.aspx

## Slide 31: Models
Models combine information related to carbon stock estimates and activity data
Models can be empirical, for example based on existing inventory data or yield curves, or mathematical representations of processes that drive carbon losses and gains
Notes: KEY MESSAGES:
The third method of forest measurement presented was models. There are a wide variety of modeling approaches but all depend on data from remote sensing and/ or field inventories as inputs.
Notes:
Models that focus on different carbon pools can be combined in order to provide an estimate of carbon transfer between pools. However, some models may themselves incorporate other models that focus on specific carbon pools better than others. It is also possible to combine global models (e.g. NASA models on global NPP or BIOME BGC) with local models so that global models feed results into more localized models. Improvements to existing models and new models are continuously being developed and combined to better meet information requirements.

## Slide 32: Models
Examples of a wide range of models that are used to estimate carbon losses and gains
Notes: KEY MESSAGES:
Models refer to a wide range of approaches, empirical or mathematical in nature. Models use a variety of data inputs to estimate changes in carbon pools at a variety of spatial and temporal scales. Some example models are provided as shown in the table.
Chart source:
Havemann, T. 2009. Measuring and Monitoring Terrestrial Carbon: The State of the Science and Implications for Policy Makers ion to calculate biomass and carbon pools. Report for the Terrestrial Carbon Group and the UNREDD Programme

## Slide 33: Comparison of Methods for Terrestrial Carbon Measurement
Method | What can it do? | Pros | Cons
Field measurements | Carbon density, areal extent, change over time if measured more than once | Precise for measured variable, Low technology requirement Can be inexpensive depending on labor cost | Costs related to labor and area, Limited to measurable variables, Can be slow, May not provide results that are consistent over a large area Accuracy may depend on conversion values applied
Notes: KEY MESSAGES:
In the next three slides there will be a review comparison of the three methods presented for C measurement- a good chance to review the three basic approaches their pros and cons.

## Slide 34: Comparison of Methods for Terrestrial Carbon Measurement
Method | What can it do? | Pros | Cons
Remote sensing | Areal extent, volume and change over time if measured more than once. | May be cost-effective, Supports field work performance, Transparent interpretation methodologies, Can be routinely collected, if available, Globally consistent, Accurate for area estimation | Some forms of sensor may not be suitable for tropical forests, Can be technically demanding, can be expensive to interpret results Not all forms of remote sensing is available for all regions Not suitable for estimating stocks
Notes: KEY MESSAGES:
Comparison of three methods for C measurement

## Slide 35: Comparison of Methods for Terrestrial Carbon Measurement
Method | What can it do? | Pros | Cons
Models | Combine information to derive carbon volumes | Framework for integrating various types of data | Accuracy is dependent on quality of input data
Notes: KEY MESSAGES:
We have talked about three major classes of measurement and monitoring methods but it is important to think of the different approaches as complementary not exclusive. A good system will include multiple approaches. Highlight an integration of different methods eg. RS and field method

## Slide 36: Integration of Methods for Terrestrial Carbon Measurement
Notes: KEY MESSAGES:
Multiple methods should be integrated into a complete system for terrestrial carbon measurement and monitoring
We have talked about three major classes of measurement and monitoring methods but it is important to think of the different approaches as complementary not exclusive. A good system will include multiple approaches.
Image source:
Havemann, T. 2009. Measuring and Monitoring Terrestrial Carbon: The State of the Science and Implications for Policy Makers Report for the Terrestrial Carbon Group and the UNREDD Programme

## Slide 37: Take Home Message
Terrestrial carbon measurement and monitoring relies on three approaches:
  Field measurements
  Remote sensing
  Models
Each approach has pros and cons and a strong measurement system integrates multiple approaches

## Slide 38: References and Resources
USAID. 2015. USAID LEAF‘s Climate Change Curriculum. USAID Lowering Emissions in Asia Forests Program (USAID LEAF). Winrock International and US Forest Service. Bangkok, Thailand.
FAO. 2010. Forest Genetic Resources Assessment 2010: Main Report. Food and Agriculture Organization of The United Nations, Rome.
FAO. 2012. Community Guidelines for Accessing Forestry Voluntary Carbon Markets. RAP Publication 2012/16. Food and Agriculture Organization of The United Nations, Rome.
Brown S. et al. 1997. Estimating Biomass and Biomass Change of Tropical Forests: a Primer. (FAO Forestry Paper - 134) FAO Food and Agriculature Organization of the United Nations Rome. http://www.fao.org/docrep/w4095e/w4095e00.HTM
Watson, C. 2009. Forest carbon accounting: overview & principles. UNDP: CDM Capacity Development in Eastern and Southern Africa. Available Source: http://www.undp.org/climatechange/carbon-finance/Docs/Forest%20Carbon%20Accounting%20-%20Overview%20&%20Principles.pdf
2006 IPCC Revised Guidelines for National Greenhouse Gas Inventory: http://www.ipcc-nggip.iges.or.jp/public/2006gl/
Havemann, T. 2009. Measuring and Monitoring Terrestrial Carbon: The State of the Science and Implications for Policy Makers Report for the Terrestrial Carbon Group and the UNREDD Programme

## Slide 39: References and Resources
The curriculum of USAID’s Climate-Resilient Ecosystems and Livelihoods (CREL) in Bangladesh is a free resource of teaching materials for university professors, teachers and climate change training experts.
Reproduction of CREL’s curriculum materials for educational or other non-commercial purposes is authorized without prior written permission from the copyright holder, provided the source is fully acknowledged.
Suggested citation: Winrock International. 2016. USAID‘s Climate-Resilient Ecosystems and Livelihoods (CREL). Winrock International. Dhaka, Bangladesh.
Disclaimer: The CREL’s curriculum is made possible by the support of the American People through the United States Agency for International Development (USAID). The contents of the curriculum do not necessarily reflect the views of USAID or the US Government.

## Slide 40: USAID's Climate-Resilient Ecosystems and Livelihoods (CREL) Project Winrock International Headquarters 2101 Riverfront Drive, Little Rock Arkansas 72202-1748 USA Tel: 1-501-280-3000 Web: www.winrock.org